# Final report

## Project details

| Project title | GREENSHIP Demonstration project |
| --- | --- |
| Project identification (program abbrev. and file) | EUDP File: 1440-0008 |
| Name of the programme which has funded the project | EUDP - GREENSHIP |
| Project managing company/institution (name and address) | A.P. Møller Mærsk A/S Esplanaden 50 1098 Copenhagen K |
| Project partners | Optivation ApS |
| CVR (central business register) | 22756214 |
| Date for submission | 10-05-2017 |

## Short description of project objective and results

The maximum possible utilisation of vessel capacity depends on the cargo composition accepted. One objective of the uptake management team is to maximize the intake of vessels by accepting the best available cargo while considering stowage rules and limitations. A good cargo composition consists of a mix of light and heavy containers to ensure the stability of the vessel and to lose as few slots as possible.

The cargo mix optimization model provides valuable information on the current utilisation of a vessel and decision support for the acceptance or denial of bookings. Besides an estimation of the total capacity consumption, a factor for each booking is provided that predicts the actual weight capacity usage.

Dansk:

Den maksimale udnyttelse af et skibs kapacitet afhænger direkte af hvordan lasten fordeler sig på tværs af vægt- og produkt-kategorier.

Et af formålene for Uptake Management (UTM) teamet er således at udvælge den bedst mulige fragt-kombination, under hensyntagen til stuvningsregler og begrænsninger.

Et godt fragt-mix (cargo composition) består altså af en fornuftig blanding af lette og tunge containere, som maksimerer de udnyttede slots ombord og samtidig sikrer skibets stabilitet.

Cargo Mix Optimisation modellen giver i denne forbindelse UTM teamet værdifuld information om den nuværende udnyttelse af skibet, samt beslutningsstøtte til teamet omkring accept eller afvisning af potentiel fragt.

Udover en estimering af forventet totalt kapacitetsforbrug for et givet mix, så er det i modellen muligt at tildele hver booking (potentiel fragt) en værdi, som nøjagtigt beskriver dét antal standard container slots, den pågældende booking vil forbruge.

References

http://www.maersk.com/en/the-maersk-group/about-us/publications/group-annual-magazine/2016/welcome-to-the-future-maersk-app-store

http://www.maersk.com/en/markets/2017/04/maersk-partners-with-microsoft-to-power-digital

Capital Markets Day 2016 (December 13, 2016)

http://files.shareholder.com/downloads/ABEA-3GG91Y/4004919352x0x920931/5F45D673-AD7D-43FC-A6C0-7548D2069ADC/Transport_and_Logistics_CMD_2016.pdf (Slides 55-65)